## Slide 1: Planning for energy storage and microgrids
Pacific Northwest National Laboratory
Distribution Systems and Planning Training
for NASUCA
October 30, 2020
Jeremy Twitchell

## Slide 2: Agenda
Technology Overview
Services and Valuation
Energy Storage in Regional Markets
Storage in Microgrids

## Slide 3
Technology Overview

## Slide 4: Storage Technologies: Mechanical
Electricity is stored as potential energy that is later used to generate electricity.
Pumped-Storage Hydro (PSH)
Long duration (8+ hours)
Good round-trip efficiency (RTE) – 80%
Cycle life: 15,000 (40+ years)
Limited flexibility
Compressed Air Energy Storage
Long duration (8+ hours)
Low RTE (~50%)
Cycle life: 10,000 (~25 years)
Limited flexibility
Short duration (~15 min)
Very good RTE (~85%)
Cycle life: 200,000 (~20 years)
Highly flexible
Flywheels
Ridge Energy Storage & Grid Services LP

## Slide 5: Storage Technologies: Electrochemical
Electricity is stored in chemical bonds and later released.
Short to mid-range duration (0.5 - 4 hours)
Very good round-trip efficiency (RTE) – 86%
Cycle life: 3,500 (7-10 years)
Highly flexible
Developed supply chain
Safety concerns
Recycling challenges
Lithium-ion Batteries
Flow Batteries
Moderate durations (4-8 hours)
Moderate round-trip efficiency (RTE) – 70%
Cycle life: 10,000 (15-20 years)
Highly flexible
Improved safety
Highly recyclable
Mechanical challenges
Sodium Batteries
Moderate durations (4-6 hours)
Good round-trip efficiency (RTE) – 75%
Cycle life: 4,000 (10-13 years)
Highly flexible
High-temperature ops

## Slide 6: Storage Technologies: Thermal
Electricity is stored by heating/cooling air or another medium for energy management or electricity production.
Moves energy through time, but does not inject electricity into the grid
Moderate duration (4-6 hours)
Can shift up to 95% of HVAC loads to off-peak
Ice thermal storage
Concentrating Solar
Longer duration (6-12 hours)
Very good RTE – 86% (Hameer and Van Niekerk 2016)
Moderate life (20-30 years)
Moderately flexible (turbine generator)
Ice Energy, Inc.
U.S. DOE

## Slide 7: Current Installed Capacity – U.S.
Chart: 
| Pumped Hydro | Thermal | CAES | Hydrogen | Li-ion | Lead Acid | Nickel | Sodium | Flow
Column1 | 0.92794 | 0.027439 | 0.0046684 | 1e-07 | 0.032588 | 0.0019968 | 0.001114 | 0.0010515 | 0.00017801
Column2
Pumped Hydro | 22.6 GW
Battery | 0.9 GW
Thermal | 0.7 GW
Compressed Air | 0.1 GW
Total | 24.3 GW
Lithium-Ion | 792 MW
Lead Acid | 49 MW
Nickel | 40 MW
Sodium | 26 MW
Flow | 4 MW
Flywheel | 58 MW
Capacitor | 2 MW
Pumped Hydro (92.8%)
Thermal (2.7%)
Battery (4%)
Compressed Air (0.5%)
Total Battery Capacity
Lithium-Ion
(88.2%)
Sodium(2.8%)
Nickel (3%)
Flow (0.5%)
Lead Acid
(5.4%)
Sources:
DOE Global Energy Storage Database (https://www.sandia.gov/ess-ssl/global-energy-storage-database-home/);
EIA Form 860 Data (https://www.eia.gov/electricity/data/eia860/)
Total Energy Storage Capacity

## Slide 8: Interconnection and Control Infrastructure
Battery storage prices are generally given based on the battery itself, but interconnecting the device to the grid and allowing for control and interoperability requires additional infrastructure (and cost):
Battery capacity:
$271/kWh
($1,084/kW)
Example 4-hour lithium-ion project
Power Conversion: $288/kW ($72/kWh)
Balance of Plant (controls, switches, HVAC, etc.):
$100/kW
($25/kWh)
Construction & Commissioning:
$101/kW
($25/kWh)
Total all-in cost for a 4-hour li-ion battery: $469/kWh, $1,876/kW
DOE/EPRI 2013 Electricity Storage Handbook in Collaboration with NRECA

## Slide 9
Services and Valuation

## Slide 10: Energy Storage Services
Distribution Services
Voltage support
Conservation voltage reduction
DG integration/hosting capacity
Flow management
Infrastructure deferral
Transmission Services
Thermal management
Congestion relief
Infrastructure deferral
Generation Services
Capacity
Energy
Ancillary services
  Regulation
  Frequency response
  Spin/non-spin reserve
  Etc. …
Customer Services
TOU rate management
Demand charge reduction
Power quality
Resilience
Image: U.S. Department of Energy, “Grid Modernization Multi-Year Program Plan”

## Slide 11: Energy Storage Values
Storage values are locational, subject to:
Resource mix
Local infrastructure
Contingency conditions
Utility tariffs
Market structure
Balducci et al, “Assigning Value to Energy Storage Systems at Multiple Points in an Electric Grid.”

## Slide 12: A Different Paradigm: Embedded Energy Storage
Electricity is unique among commodities in that its “supply chain” was developed without a storage component.
Every other commodity has the ability to store excess quantities built into its supply chain – warehouses, granaries, reservoirs, etc.
Embedded storage creates a buffer between mismatches in supply and demand, stabilizing prices and protecting customers.
Question: Now that we have the technology to store electricity, should we retrofit the grid with it?
To date, energy storage has been added “on the margins” to impart flexibility to the grid.
If storage were embedded infrastructure, similar to a substation or a transformer, it could act as a natural buffer between mismatches in supply and demand and the grid would be flexible.
First report available here; watch PNNL’s Grid Architecture site for additional reports in the series

## Slide 13: Embedded Storage in the Natural Gas System
A simple comparison: Natural gas and electricity
Simple assumptions: City has average daily demand of 1 million cubic feet (CF) of natural gas, peaking to 1.5 million CF; average electricity demand of 100 MW, peaking to 125 MW
Result: Embedded storage on the natural gas system means that pipelines upstream of the storage facility can be sized based on average demand, and only downstream pipelines need to be sized based on peak.
On the electric side, the entire system (generation, transmission, and distribution) serving the city must be designed based on peak demand.
Adapted from Aspen Environmental Group

## Slide 14
Energy Storage in Regional Markets

## Slide 15: Energy Storage and Regional Markets
The Federal Energy Regulatory Commission (FERC) has two primary areas of regulatory authority over the electric grid:
Market design and operations in the deregulated market footprints (minus ERCOT)
Transmission system planning, operations, and ratemaking in all regions with interstate transmission
In recent years, FERC has sought to improve access for energy storage in both areas.

## Slide 16: Market Access: FERC Order 841
In February 2018, FERC issued Order 841 to “remove barriers to the participation of electric storage resources in the capacity, energy, and ancillary service markets operated by Regional Transmission Organizations (RTO) and Independent System Operators (ISO).”
Filings must meet seven criteria:
Create a participation model;
Make storage eligible to participate in all applicable markets;
Account for the physical and operational characteristics of storage resources;
Allow storage owners to self-manage their state of charge;
Establish a minimum size requirement no greater than 100 kW;
Accurately meter and charge storage devices when charging (wholesale rates, no transmission charges when directed to charge by ISO); and
Have an effective date within one year of FERC acceptance unless more time is reasonably necessary.

## Slide 17: Transmission Access: FERC Policy Statement
Prompted by two proceedings involving PSH facilities
  Nevada Hydro (2008): FERC rejects developer’s petition to build a pumped storage hydro (PSH) project and require California Independent System Operator (CAISO) to assume operational control and operate it as a transmission asset; bid in market at $0
  Western Grid (2010): FERC approves developer’s petition to build a PSH project that will be operated as a transmission asset at CAISO’s direction, no market bids
Policy Statement: Storage can be a dual-use (transmission and generation) asset, subject to three clarifying principles:
  Avoid double recovery of costs
  Minimize adverse impacts on markets
  ISO/RTO independence must not be compromised
A policy statement is a nonbinding document; no action required
  CAISO and MISO were the only entities to initiate a direct response to statement

## Slide 18
Storage in Microgrids

## Slide 19: Storage and Microgrids: A New Resilience Paradigm
The advent of cost-competitive energy storage options has enabled us to go from:
  Limited opportunities for grid participation
  High cost
  Limited to facilities in which resilience is mission critical
Mission-critical Resilience
Capacity
Energy
Economic Resilience
Capacity
Energy
Regulation
Reserves
Arbitrage
…
to
  Increased opportunities for grid participation
  Offsetting revenues reduce system costs
  Viable resilience for broader range of facilities

## Slide 20: Questions States Can Ask
Are planning tools accounting for the granular values and operational characteristics of energy storage technologies?
Are tariffs and rates in place to incent customers who deploy storage and other distributed energy resources to use those assets in a way that benefit the grid and reduce system costs?
Can tariffs be used to incent development and grid-beneficial use of microgrids?
What plans are in place for end-of-life disposal of battery assets?
Absent resilience metrics, how can planning processes be adapted to meet resilience goals in a cost-effective manner?
Are there opportunities for furthering state goals through increased engagement in RTO/ISO processes?

## Slide 21
Questions?
Jeremy Twitchell
jeremy.twitchell@pnnl.gov
971-940-7104

## Slide 22
Appendix Slides

## Slide 23: Resources for More Information
Y Xu, CC Liu, KP Schneider, FK Tuffner, DT Ton: Microgrids for Service Restoration to Critical Load in a Resilient Distribution System
Schneider et al., Preliminary Design Process for Networked Microgrids
M Armendariz et al., Coordinated Microgrid Investment and Planning Processes Considering the System Operator
JB Twitchell, RS O’Neil, MT McDonnell, Report: Planning Considerations for Energy Storage in Resilience Applications
B Ward et al., The Advanced Microgrid: Integration and Operability
Schwartz, Lisa C, and Greg Leventis. Grid-Interactive Efficient Buildings: An Introduction for State and Local Governments
Eckman, Tom, Lisa C Schwartz, and Greg Leventis. Determining Utility System Value of Demand Flexibility From Grid-interactive Efficient Buildings
Schiller, Steven R, Lisa C Schwartz, and Sean Murphy. Performance Assessments of Demand Flexibility from Grid-Interactive Efficient Buildings: Issues and Considerations
PNNL energy storage site: https://www.pnnl.gov/energy-storage
Sandia National Laboratories energy storage site: https://www.sandia.gov/ess-ssl/
LBNL Electricity Markets & Policy Group: https://emp.lbl.gov/

## Slide 24: Storage Technologies: Additional Information
Mongird et al, Energy Storage Technology and Cost Characterization Report. http://energystorage.pnnl.gov/pdf/PNNL-28866.pdf.

## Slide 25: Questions Raised by Embedded Storage
Theoretically, embedded storage could facilitate more efficient design and use of the electric grid and reduce costs by managing volatility (no daily price swings, reduced need for ancillary services, etc.).
Several regulatory barriers exist:
Lack of underlying standards (not contemplated in reliability standards; no resilience standards)
Inclusion in planning processes (regional transmission planning processes are generally slow to integrate new technologies)
Ownership models (security and control issues complicate third-party ownership)
Compensation structure (current market structures not designed to value this kind of service; lack of standards means it’s difficult to make a case for it as a regulated asset)
Metrics (how do you measure a buffer?)
Valuing this type of asset is something we’re just starting to think about:
How would you quantify its impacts on the grid and compensate them?
Valuation will be the focus of a forthcoming paper.

## Slide 26: Storage as Transmission: Case Study
The 2019 MISO Transmission Expansion Plan (MTEP) was the second regional transmission plan to select energy storage as a transmission asset
Storage as Transmission: Waupaca, WI
  Under certain N-1 contingency scenarios, the Waupaca area would be cut off
  At $12.2 million over 40 years, a 2.5 MW/5 MWh energy storage system, coupled with line sectionalization, was selected over a $13.1 million project to install an additional circuit
  Expected in-service date: Dec. 2021
As a transmission asset, the storage system’s costs will be recovered through MISO’s FERC-approved transmission system rates, and it will not participate in energy markets.